## Slide 1: Arithmetic Hardware

## Slide 2: Introduction
Adders
  Half
  Full
  Ripple-Carry
  Carry-Lookahead
  Carry-Select
Arithmetic Logic Unit

## Slide 3: 1-Bit Half Adder
Sum = A’B + AB’
Cout = AB
A | B | Sum | Cout
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 4: 1-Bit Half Adder

## Slide 5: 1-Bit Half Adder
Sum = A’B + AB’
= A XOR B

## Slide 6: 1-Bit Half Adder
Block Diagram

## Slide 7: 1-Bit Full Adder
Sum = A XOR B XOR Cin
Cout = AB + ACin + BCin
Inputs |  |  | Outputs |  | Comments
A | B | Cin | Cout | Sum | 
0 | 0 | 0 | 0 | 0 | 0+0+0=00
0 | 0 | 1 | 0 | 1 | 0+0+1=01
0 | 1 | 0 | 0 | 1 | 0+1+0=01
0 | 1 | 1 | 1 | 0 | 0+1+1=10
1 | 0 | 0 | 0 | 1 | 1+0+0=01
1 | 0 | 1 | 1 | 0 | 1+0+1=10
1 | 1 | 0 | 1 | 0 | 1+1+0=10
1 | 1 | 1 | 1 | 1 | 1+1+1=11

## Slide 8: 1-Bit Full Adder
Cout = A B + Cin (A or B) = A B + B Cin + A Cin
A
B
Cin
S
A
A
B
B
Cin
Cout
Standard approach
  6 gates
  2 XORs, 2 ANDs, 2 ORs

## Slide 9: 1-Bit Full Adder
Alternative implementation
  5 gates
  half adder is an XOR gate and AND gate
  2 XORs, 2 ANDs, 1 OR
A
B
A xor B
Cin
A xor B xor Cin
Half Adder
Cout
Cin (A xor B)
A B
Sum
Cout
Half Adder
Sum
Cout

## Slide 10: 1-Bit Full Adder

## Slide 11: Ripple-Carry Adder
To add binary numbers of lengths greater than 1, we cascade one bit adders together.
A
B
Cout
Sum
Cin
0
A0
B0
Overflow
A
B
Cout
Sum
Cin
A1
B1
A
B
Cout
Sum
Cin
A2
B2
A
B
Cout
Sum
Cin
A3
B3
S3
S2
S1
S0

## Slide 12: Ripple-Carry Adder: Example
3+2 = 5
0011 + 0010 = 0101
A
B
Cout
Sum
Cin
0
A0
B0
Overflow
A
B
Cout
Sum
Cin
A1
B1
A
B
Cout
Sum
Cin
A2
B2
A
B
Cout
Sum
Cin
A3
B3
S3
S2
S1
S0
0
0
0
0
1
1
1
0
1
0
0
1
1
0
0
0
0

## Slide 13: Ripple-Carry Adder: Subtraction
Use adders to subtract with 2s complement representation
  A – B = A + (– B) = A + B' + 1
A
B
Cout
Sum
Cin
0
1
0 = Add 1 = Subtract
A0
B0
B0'
Sel
Overflow
A
B
Cout
Sum
Cin
A1
B1
B1'
Sel
A
B
Cout
Sum
Cin
A2
B2
B2'
Sel
0
1
0
1
0
1
A
B
Cout
Sum
Cin
A3
B3
B3'
Sel
S3
S2
S1
S0

## Slide 14: Ripple-Carry Adder: Subtraction
7 – 6 = 1
0111 – 0110 = 0001
A
B
Cout
Sum
Cin
0
1
A0
B0
B0'
Sel
Overflow
A
B
Cout
Sum
Cin
A1
B1
B1'
Sel
A
B
Cout
Sum
Cin
A2
B2
B2'
Sel
0
1
0
1
0
1
A
B
Cout
Sum
Cin
A3
B3
B3'
Sel
S3
S2
S1
S0
0
0
1
1
1
0
1
1
0
1
0
1
1
1
1
1
1
1
0
1
0
1
0
1
0
1
1
0
0
1
0

## Slide 15: Ripple-Carry Adder: Disadvantage
Long Delay
  Carry bit may have to propagate from LSB to MSB
  Worst case delay for n-bit adder = 2n gate delays
COut3
A0
B0
1-bit
Result0
COut0
A1
B1
1-bit
Result1
CIn1
COut1
A2
B2
1-bit
Result2
CIn2
A3
B3
1-bit
Result3
CIn3
COut2
CIn0
CIn
COut
A
B
n
2 gates/level

## Slide 16: Ripple-Carry Adder
Long delay due to the propagation of carry from low to high order stages
The key to speeding up addition is determining carry values sooner.

## Slide 17: Carry-Lookahead
Determine the CarryOut:
  Cout = AB + ACin + BCin = AB + Cin(A+B)
A | B | Cout | Comment
0 | 0 | 0 | Carry terminate
0 | 1 | Cin | Carry propagate
1 | 0 | Cin | Carry propagate
1 | 1 | 1 | Carry generate

## Slide 18: Carry-Lookahead Logic
Carry generate: Gi = Ai Bi
  Must generate carry when A = B = 1
Carry propagate: Pi = Ai + Bi
  Carry-in will equal carry-out here
Cout can be re-expressed these terms:
  Ci+1 = Ai Bi + Ai Ci + Bi Ci = Ai Bi + Ci (Ai + Bi) = Gi + Ci Pi

## Slide 19: Carry-Lookahead Logic
Assume we have a 4-bit adder:
  C1 = G0 + P0 C0
  C2 = G1 + P1 C1 = G1 + P1 G0 + P1 P0 C0
  C3 = G2 + P2 C2 = G2 + P2 G1 + P2 P1 G0 + P2 P1 P0 C0
  C4 = G3 + P3 C3 = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0 + P3 P2 P1 P0 C0
Each of the carry equations can be implemented with two-level logic
  All inputs are now directly derived from data inputs and not from intermediate carries
  this allows computation of all sum outputs to proceed in parallel

## Slide 20: Carry-Lookahead Implementation
G3
C0
C0
C0
C0
P0
P0
P0
P0
G0
G0
G0
G0
C1
P1
P1
P1
P1
P1
P1
G1
G1
G1
C2
P2
P2
P2
P2
P2
P2
G2
G2
C3
P3
P3
P3
P3
C4
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay
increasingly complex logic for carries
Adder with propagate and generate outputs

## Slide 21: Partial Carry Lookahead Adder
Very expensive to build “full” carry lookahead adder
  Imagine the length of the equation for Cin31!
In practice:
  Connect several N-bit lookahead adders
  Example: four 8-bit carry lookahead adders can form a 32-bit partial carry lookahead adder
8-bit Carry
Lookahead
Adder
C0
8
8
8
Result[7:0]
B[7:0]
A[7:0]
8-bit Carry
Lookahead
Adder
C8
8
8
8
Result[15:8]
B[15:8]
A[15:8]
8-bit Carry
Lookahead
Adder
C16
8
8
8
Result[23:16]
B[23:16]
A[23:16]
8-bit Carry
Lookahead
Adder
C24
8
8
8
Result[31:24]
B[31:24]
A[31:24]

## Slide 22: Carry-Select Adder
4-Bit Adder [3:0]
C0
C4
4-bit adder [7:4]
1
C8
0
C8
five 2:1 mux
0
1
0
1
0
1
0
1
adder low
adder high
0
1
4-bit adder [7:4]
C8
S7
S6
S5
S4
S3
S2
S1
S0
Redundant hardware to make carry calculation go faster
  Compute two high-order sums in parallel while waiting for carry-in
  One assuming carry-in is 0 and another assuming carry-in is 1
  Select correct result once carry-in is finally computed

## Slide 23: Arithmetic Logic Unit
The Arithmetic Logic Unit (ALU) is the brawn of the computer
  Performs arithmetic operations (addition, subtraction)
  Performs logical operations (AND, OR, NOR)
  Performs logical comparisons (Less Than, Equal To)

## Slide 24: Arithmetic Logic Unit
We will need (at least) a 32-bit ALU
  Connect 32 1-bit ALUs together

## Slide 25: AND, OR
Uses: AND gate, OR gate, 2:1 mux

## Slide 26: Addition
Add a 1-bit full adder

## Slide 27: Addition
This 1-bit ALU will perform AND, OR, and ADD

## Slide 28: Subtraction
(A – B) is equivalent to A + (–B)
  Take 2’s complement of B and add A
  2’s Complement: invert every bit and add 1
To invert B
  Add a 2:1 mux that chooses between b and b’
To add 1
  Set the CarryIn to 1 instead of 0

## Slide 29: Subtraction

## Slide 30: NOR
NOR = NOT (A OR B)
= (A + B)’
= A’*B’
= A’ AND B’
We already have an AND gate and an inverter for B
  Add an inverter for A

## Slide 31: NOR

## Slide 32: Set on Less Than
Set on Less Than (slt) is a MIPS instruction
For inputs A and B it produces 1 if A<B, 0 otherwise
All bits are set to zero except for the least significant
  Least significant bit determined by the result of A<B

## Slide 33: Set on Less Than
For our ALU to perform this operation we need:
  A bigger mux
  Input for the slt (called Less)
  Method for determining if A<B

## Slide 34: Set on Less Than
A < B
A-B < 0
  Subtract and check the sign of the result
  1 if less than 0
  0 otherwise

## Slide 35: Set on Less Than
Bits 1-31: Less = 0
Bit 0: sign bit of A-B

## Slide 36: Set on Less Than
“Set” generate by most significant bit:

## Slide 37: Equal To
A = B
A-B = 0
  Subtract and check to see if all bits are zero
  NOR all bits

## Slide 38: Equal To
Zero Detection Logic is just a NOR gate
  Output true (1) only if all inputs zero
CIn0
A0
B0
1-bit
ALU
Result0
COut0
A1
B1
1-bit
ALU
Result1
CIn1
COut1
A2
B2
1-bit
ALU
Result2
CIn2
COut2
A3
B3
1-bit
ALU
Result3
CIn3
COut3
Zero

## Slide 39: A 32-Bit ALU
Connect:
  31 ALUs without overflow detection
  1 ALU with overflow detection (MSB)

## Slide 40: A 32-Bit ALU
Subtraction:
  Both CarryIn and Binvert are 1
  Combine into 1 signal “Bnegate”

## Slide 41: A 32-Bit ALU
Set on Less Than:
  Less = 0 Bits 1-31
  Less = sign bit Bit 0

## Slide 42: A 32-Bit ALU
Universal symbol for ALU