## Slide 1: MIPS
Instruction Set Architecture

## Slide 2: Introduction
Hardware
  Voltages
  Logic Gates
  Latches
  Flip-Flops
  Registers
  Adders
  Arithmetic Logic Unit

## Slide 3: Introduction
Hardware Languages
  Instruction Sets
  MIPS Assembly Language
  Machine Code
    Binary
    Hexadecimal

## Slide 4: Instruction Set
Instructions: the words of a computer language
Instruction set: vocabulary
  Repertoire of instructions of a computer
Instruction sets may differ from computer to computer, but have many things in common.
  Computational operations
  Memory access & addressing
  Branches
  Procedure calls

## Slide 5: MIPS Instruction Set
All instruction sets promote a common goal.
  Make it easy to build the hardware and the compiler while maximizing performance and minimizing cost.
MIPS is a popular instruction set and still has a share of the embedded core market

## Slide 6: Arithmetic Operations
Addition
add a, b, c
a = b + c

## Slide 7: Arithmetic Operations
Each instruction performs only one operation.
Each instruction must have three variables.
  Two sources and one destination.

## Slide 8: Arithmetic Operations
a = b + c + d + e
add a, b, c #a = b + c
add a, a, d #a = b + c + d add a, a, e #a = b + c + d + e

## Slide 9: Arithmetic Operations
Each line can only have one instruction on it
Anything following a # is a comment.

## Slide 10: Arithmetic Operations
From C to MIPS
a = b + c; d = a – e;
add a, b, c sub d, a, e

## Slide 11: Arithmetic Operations
From C to MIPS
f = (g + h) – (i + j);
add t0, g, h #temporary variable t0 = g + h
add t1, i, j #temporary variable t1 = i + j
sub f, t0, t1 #f = t0 – t1

## Slide 12: Operands
Instructions use register operands
Registers
  Made from Flip-Flops
  Primitive used in hardware design
Register Size
  32 bits
  Called a “word”
Number of Registers
  32 registers in the register file
  Use for frequently accessed data
  Numbered 0 to 31

## Slide 13: Operands
MIPS naming conventions
  $00 - $31
  $XX
    A $ followed by two characters that represent the register
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables

## Slide 14: Arithmetic Operations
From C to MIPS
f = (g + h) – (i + j);
f g h i j $s0 $s1 $s2 $s3 $s4
add $t0, $s1, $s2 #temporary variable t0 = g + h
add $t1, $s3, $s4 #temporary variable t1 = i + j
sub $s0, $t0, $t1 #f = t0 – t1

## Slide 15: Memory Operands
Simple variables
  Integers, Characters, etc.
Data Structures
  Arrays, Structures
Store data structures in main memory

## Slide 16: Memory Operands
To use data from main memory:
  Load values from memory into registers
  Store result from register to memory

## Slide 17: Memory Operands
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4

## Slide 18: Memory Operands
load
  Copies data from memory to a register
store
  Copies data from a register to memory

## Slide 19: Memory Operands
lw destination, constant(register)
The “load word” instruction takes the sum of the constant and the register to determine a memory address. The data at this address is placed in the destination register.

## Slide 20: Memory Operands
From C to MIPS
  A is an array of 100 words
  g is a variable in $s1
  h is a variables in $s2
  base address of A is in $s3
  g = h + A[8];
First, we have to transfer A[8] to a register.
A[8] is stored in memory address $s3 + 8*4
lw $t0, 32($s3) # t0 = A[8]
add $s1, $s2, $t0 # g = h + A[8]
Offset
Base Register

## Slide 21: Memory Operands
sw data, constant(register)
The “store word” instruction takes the sum of the constant and the register to determine a memory address. The data in the first register operand will be placed at this address.

## Slide 22: Memory Operands
From C to MIPS
  A is an array of 100 words
  h is a variables in $s2
  base address of A is in $s3
A[12] = h + A[8]
lw $t0, 32($s3) # t0 = A[8]
add $t0, $s2, $t0 # t0 = h + A[8] sw $t0, 48($s3) # store t0 in A[12]

## Slide 23: Constant Operands
Sometimes we need to use a constant value
So far, we would need to load the constant into a register
  Requires two instructions: load word and add
Instead, the “add immediate” instruction allows us to use a constant instead of one of the register operands

## Slide 24: Constant Operands
From C to MIPS
s = s + 4
addi $s0, $s0, 4

## Slide 25: Representing Instructions
We know that computers use binary to represent data
Register names are also mapped to numbers
08 $t0 16 $s0
09 $t1 17 $s1
10 $t2 18 $s2
11 $t3 19 $s3
12 $t4 20 $s4
13 $t5 21 $s5
14 $t6 22 $s6
15 $t7 23 $s7

## Slide 26: Representing Instructions
C Programming Language
  fruit = num_apples + num_oranges;
MIPS Assembly
  add $s0, $s1, $s2
Machine Code
  0000 0010 0011 0010 1000 0000 0010 0000

## Slide 27: Representing Instructions
Instruction Format
  The layout of an instruction
  formed by pieces of the instruction called fields

## Slide 28: Representing Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 29: Representing Instructions
add $t0, $s1, $s2
Represented using decimal numbers in each field:
Convert each field to binary:
Result:
000000100011001001000000001000002
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000

## Slide 30: Representing Instructions
Hexadecimal
  Instead of writing strings of 32-bit binary numbers, we can use hexadecimal – a base that converts easily into binary.
  Hexadecimal is base 16
    Uses digits 0-9, A-F
    Replaces a group of four binary numbers with a single hexadecimal digit
0 | 0000 | 4 | 0100 | 8 | 1000 | C | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | D | 1101
2 | 0010 | 6 | 0110 | A | 1010 | E | 1110
3 | 0011 | 7 | 0111 | B | 1011 | F | 1111

## Slide 31: Representing Instructions
add $t0, $s1, $s2
000000100011001001000000001000002
0000 0010 0011 0010 0100 0000 0010 0000
0 2 3 2 4 0 2 0
0x02324020

## Slide 32: Representing Instructions
Convert from hexadecimal to binary:
0xECA86420
E C A 8 6 4 2 0
1110 1100 1010 1000 0110 0100 0010 0000

## Slide 33: Instruction Formats
What if we need longer fields?
  The load word instruction specifies two registers and a constant.
  With our current fields, the constant is restricted to 5 or 6 bits
Same size for all instructions vs. Same format for all instructions
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 34: Instruction Formats
R-type
I-type
J-type
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
op
address
6 bits
26 bits

## Slide 35: Instruction Formats
I-type
A 16 bit address allows:
  lw and sw to access a range of 8192 words
  addi to add constants in a range of +/- 215
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 36: Instruction Formats
lw $t0, 32($s3)
Represented using decimal:
35 19 8 32
Represented in binary:
100011 10011 01000 0000000000100000
1000 1110 0110 1000 0000 0000 0010 0000
Represented in hexadecimal:
0x8E680020
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 37: Instruction Formats
Different formats complicate decoding, but allow 32-bit instructions uniformly
Keep formats as similar as possible
  First three fields of R-type and I-type are the same
  Fourth field of I-type is the size of the last 3 fields of R-type
The first field (op) determines the type and is the same in all three formats

## Slide 38: From C to Machine Code
A[300] = h + A[300];
lw $t0, 1200($t1) #$t1 is the base register
add $t0, $s2, $t0 #$s2 is h
sw $t0, 1200($t1)
35 9 8 1200
0 18 8 8 0 32
43 9 8 1200

## Slide 39: From C to Machine Code
A[300] = h + A[300];
lw $t0, 1200($t1) #$t1 is the base register
add $t0, $s2, $t0 #$s2 is h
sw $t0, 1200($t1)
100011 01001 01000 0000010010110000 000000 10010 01000 01000 00000 100000 101011 01001 01000 0000010010110000

## Slide 40: Logical Operations
Shifts
Logical Operation | C Operator | MIPS Instruction
Shift Left | << | sll
Shift Right | >> | srl

## Slide 41: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 42: Shift Operations
0000 0000 0000 00000 000 0000 0000 0000 1001 (9)
Shift left by four:
0000 0000 0000 0000 0000 0000 0000 1001 0000 (144)
9 * 24 = 144

## Slide 43: Shift Operations
sll $t2, $s0, 4 # t2 = s0 << 4
R-type instruction that uses the shamt field:
0 0 16 10 4 0

## Slide 44: Logical Operations
Logical
Logical Operation | C Operator | MIPS Instruction
Bitwise AND | & | and, andi
Bitwise OR | ¦ | or, ori
Bitwise NOT | ~ | nor

## Slide 45: AND
Bit-by-bit operation that leaves 1 in the result only if both bits of the operands are 1.
and $t0, $t1, $t2
Use AND to “mask” some bits in a word.
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 46: OR
Bit-by-bit operation that leaves 1 in the result only if either bits of the operands are 1.
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 47: NOT
Bit-by-bit operation on only one operand that inverts each bit: changes a 0 to a 1 and 1 to a 0
NOR
  NOT OR
  A NOR 0 = NOT (A OR 0) = NOT A

## Slide 48: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  move between registers
  add $t2, $s1, $zero
  NOT
  nor $t0, $t1, $zero

## Slide 49: NOT
nor $t0, $t1, $zero #t0 = ~(t1 | 0)
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0

## Slide 50: Logical Operations with Constants
and immediate
  andi
Or immediate
  ori

## Slide 51: Branches
Computer programs can make decisions
  If statements, Switch statements
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1

## Slide 52: Branches
if (i==j) f = g + h; else f = g - h;
i j f g h
$s0 $s1 $s2 $s3 $s4

## Slide 53: Branches
if (i==j) f = g + h; else f = g - h;
i $s0
j $s1
f $s2
g $s3
h $s4
bne $s0,$s1,Else add $s2,$s3,$s4
j Exit
Else: sub $s2,$s3,$s4 Exit:

## Slide 54: Loops
Some computer programs require iteration
  while loops, for loops

## Slide 55: Loops
while (save[i] == k)
i +=1;
Assume i in $s3, k in $s5, base address of save in $s6.
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit:

## Slide 56: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 57: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
beq and bne are the common case
  slt, slti, beq, bne can be used to create any other necessary conditions.
This is a good design compromise

## Slide 58: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 59: Switch Statements
switch (selection) {
case 1:
….
case 2:
…
default:
}
if (selection == 1)
goto 1
else if (selection == 2)
goto 2
else
goto 3

## Slide 60: Switch Statements
switch (selection) {
case 1:
….
case 2:
…
default:
}
Jump Address Table
selection is an index to the table
the table contains addresses
jr $s0

## Slide 61: Stored Program Computers
Instructions represented in binary
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs

## Slide 62: Procedures
We often write functions or methods
  procedures
A procedure is stored subroutine that performs a specific task based on the parameters it is provided

## Slide 63: Procedure Calling
Steps required
  Place parameters in registers
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call

## Slide 64: Registers
$a0-$a3: four argument registers
$v0-$v1: two return value registers
$ra: one return address register

## Slide 65: Procedure Call Instructions
Procedure call: jump and link
jal ProcedureLabel
  Address of following instruction put in $ra
    $ra = PC + 4
  Jumps to target address
Procedure return: jump register
jr $ra
  Copies $ra to program counter (PC)

## Slide 66: Procedures
The parent program (caller) places parameters in $a0-$a3
The caller uses jal to jump to the location of the function being called (callee) and store the return address
The callee completes its task and stores the result in $v0-$v1
The callee returns control with jr $ra

## Slide 67: Stacks
What if four argument registers and two return value registers aren’t enough?
Spilling Registers
  At the beginning of a procedure the contents of $s0-$s7 can be saved in main memory
  The procedure can then use $s0-$s7 normally
  At the end, the previous values of $s0-$s7 are retrieved from main memory
Stacks are a natural structure to allocate dynamic data for procedures

## Slide 68: Stacks
Stacks are a last-in-first-out structure
Requires a stack pointer to place/remove registers
  Adjust the pointer by one word when items are added (pushed) or removed (popped)
MIPS stack pointer is a register: $sp
  The “bottom” of the stack is the highest address and the stack “grows” from higher to lower addresses.
Push: write to main memory (at $sp)
decrement $sp
Pop: increment $sp
read from main memory (at $sp)

## Slide 69: Leaf Procedure Example
int leaf_example (int g, int h, int i, int j) {
int f;
f = (g+h) – (i+j);
return f;
}
Arguments g - j in $a0 - $a3
f in $s0 (hence, need to save $s0 on stack)
Result in $v0

## Slide 70: Leaf Procedure Example
leaf_example:
addi $sp, $sp, -12
sw $t1, 8($sp)
sw $t0, 4($sp)
sw $s0, 0($sp)
add $t0, $a0, $a1
add $t1, $a2, $a3
sub $s0, $t0, $t1
add $v0, $s0, $zero
lw $s0, 0($sp)
lw $t0, 4($sp)
lw $t1, 8($sp)
addi $sp, $sp, 12
jr $ra

## Slide 71: Leaf Procedure Example
To reduce register spilling, we can choose to not save and restore temporary registers.

## Slide 72: Leaf Procedure Example
leaf_example: addi $sp, $sp, -4 sw $s0, 0($sp) add $t0, $a0, $a1 add $t1, $a2, $a3 sub $s0, $t0, $t1 add $v0, $s0, $zero lw $s0, 0($sp) addi $sp, $sp, 4 jr $ra

## Slide 73: Procedures
Not all procedures are leaf procedures
  Procedures call other procedures
  Procedures call copies of themselves (recursion)
For nested call, caller needs to save on the stack:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 74: Non-Leaf Procedure Example
int fact (int n) { if (n < 1)
return 1; else
return n * fact(n - 1);
}
Argument n in $a0
Result in $v0

## Slide 75: Non-Leaf Procedure Example
fact:
addi $sp, $sp, -8 # adjust stack for 2 items
sw $ra, 4($sp) # save return address
sw $a0, 0($sp) # save argument
slti $t0, $a0, 1 # test for n < 1
beq $t0, $zero, L1
addi $v0, $zero, 1 # if so, result is 1
addi $sp, $sp, 8 # pop 2 items from stack
jr $ra # and return
L1: addi $a0, $a0, -1 # else decrement n
jal fact # recursive call
lw $a0, 0($sp) # restore original n
lw $ra, 4($sp) # and return address
addi $sp, $sp, 8 # pop 2 items from stack
mult $v0, $a0, $v0 # multiply to get result
jr $ra # and return

## Slide 76: Procedures
Preserved | Not Preserved
Saved registers: $s0-$s7 | Temporary registers: $t0-$t9
Stack pointer: $sp | Argument registers: $a0-$a3
Return address: $ra | Return value registers: $v0-$v1
Stack above the stack pointer | Stack below the stack pointer

## Slide 77: Stack Frame Layout
Arguments in reverse order
Saved registers
including
old FP, SP
Local variables
and temporaries
SP
Access local variables
and saved registers at
fixed (positive) offset
from SP
Higher Addresses
Lower Addresses
Access arguments at
fixed offset from FP. Allow variable number
of arguments.
Arguments for next procedure
FP

## Slide 78: Local Data on the Stack
Local data allocated by callee
Procedure frame (activation record)
  Used by some compilers to manage stack storage

## Slide 79: Memory Layout
Text: program code
Static data: global variables
  static variables in C
  constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  “malloc” in C
  “new” in Java
Stack: automatic storage

## Slide 80: MIPS: Software Register Convention
16 $s0 callee saves
. . .
23 $s7
24 $t8 temporary (cont’d)
25 $t9
26 $k0 reserved for OS kernel
27 $k1
28 $gp global pointer
29 $sp stack pointer
30 $fp frame pointer
31 $ra Return Address
0 $0 zero constant 0
1 $at reserved for assembler
2 $v0 expression evaluation &
3 $v1 function results
4 $a0 arguments (caller saves)
5 $a1
6 $a2
7 $a3
8 $t0 temporary: caller saves
. . .
15 $t7

## Slide 81: MIPS Register Usage and Saving
The MIPS Architecture Has General-Purpose Registers
  the usage for arguments, stack/data/global pointers, preservation, OS-reserved, etc. is a software convention

## Slide 82: MIPS Register Usage and Saving
Why are registers partitioned into caller and callee save?
The goal is to minimize the number of registers saved and restored across procedure calls
  but at the time a procedure is compiled there is generally incomplete information about register usage by the procedure’s caller and those it calls
  if the convention were purely caller save, then the caller would have to save all registers whose value will be used again, even if the callee is a simple leaf procedure that requires only the argument registers
  if the convention were purely callee save, then the callee would have to save any register it uses, even if the caller does not need the register’s value
  so an efficient compromise is a partition of caller/callee save registers

## Slide 83: Characters
Characters are represented in 8-bit bytes
  American Standard Code for Information Interchange (ASCII)
    128 characters: 95 graphic, 33 control
  Latin-1
    256 characters: ASCII characters + 96 more graphic characters
  Unicode
    Variable length: 8 bits (UTF-8), 16 bits (UTF-16), 32 bits
    Contains most of the world’s alphabets, plus symbols

## Slide 84: Characters
To load a character:
  Use load word to retrieve the correct 32 bit word
  Use logical instructions to extract the correct byte
MIPS byte instructions
  load byte
  store byte

## Slide 85: Byte Operations
load byte lb rt, offset(rs)
  Loads a byte from rs+offset, placing it in the rightmost 8 bits of rt
store byte sb rt, offset(rs)
  Stores the rightmost 8 bits of rt in rs+offset
lb $t0,0($sp) # Read byte from source
sb $t0,0($gp) # Write byte to destination

## Slide 86: Strings
Representing a string:
  the first position of the string is reserved to give the length of a string
    4 C a r t
  an accompanying variable has the length of the string
    “Cart” 4
  the last position of a string is indicated by a character used to mark the end of a string.
  C a r t \0
C programming language
Java programming language

## Slide 87: String Copy Example
void strcpy (char x[], char y[]) {
int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
Addresses of x, y in $a0, $a1
i in $s0

## Slide 88: String Copy Example
strcpy:
addi $sp, $sp, -4 # adjust stack for 1 item
sw $s0, 0($sp) # save $s0
add $s0, $zero, $zero # i = 0
L1: add $t1, $s0, $a1 # addr of y[i] in $t1
lb $t2, 0($t1) # $t2 = y[i]
add $t3, $s0, $a0 # addr of x[i] in $t3
sb $t2, 0($t3) # x[i] = y[i]
beq $t2, $zero, L2 # exit loop if y[i] == 0
addi $s0, $s0, 1 # i = i + 1
j L1 # next iteration of loop
L2: lw $s0, 0($sp) # restore saved $s0
addi $sp, $sp, 4 # pop 1 item from stack
jr $ra # and return

## Slide 89: String Copy Example
Since strcpy is a leaf procedure, we could store i in a temporary register
  Avoids saving and restoring $s0 from the stack
We can think of temporary registers as registers that the callee should use whenever convenient.
When a compiler finds a leaf procedure, it exhausts all temporary registers before using registers it must save.

## Slide 90: Halfword Operations
load halfword lh rt, offset(rs)
  Loads a halfword from rs+offset, placing it in the rightmost 16 bits of rt
store halfword sh rt, offset(rs)
  Stores the rightmost 16 bits of rt in rs+offset
lh $t0,0($sp) # Read halfword from source
sh $t0,0($gp) # Write halfword to destination

## Slide 91: Constants
Immediate-type instructions have 16 bits for constant values.
  50% to 60% of constants fit within 8 bits
  75% to 80% of constants fit within 16 bits
The occasional 32-bit constant must be loaded into a register before it can be used.
  Set the upper half of the register
    load upper immediate
  Set the lower half of the register
    or immediate

## Slide 92: 32-bit Constants
0000 0000 0011 1101 0000 1001 0000 0000
lui $s0, 61 # 61 = 0000 0000 0011 1101
$s0 = 0000 0000 0011 1101 0000 0000 0000 0000
ori $s0, $s0, 2304 # 2304 = 0000 1001 0000 0000
$s0 = 0000 0000 0011 1101 0000 1001 0000 0000

## Slide 93: 32-bit Constants
The MIPS assembler must break larger constants into pieces and reassemble them into a register.
  This is why there is one register reserved for the assembler: $at.

## Slide 94: Addressing Modes
Register Addressing
Immediate Addressing
Base Addressing
PC-Relative Addressing
Pseudodirect addressing

## Slide 95: Register Addressing
Destination of an operation is specified by a register

## Slide 96: Immediate Addressing
Destination is specified by an immediate value.
  Conditional branches specify opcode, two registers, target address
  target address is 16 bits
  If all addresses had to fit in 16 bits, programs could only be 216 words long.
op
rs
rt
address
6 bits
5 bits
5 bits
16 bits

## Slide 97: Base Addressing
Destination is determined by register + branch address

## Slide 98: PC-relative Addressing
Destination is determine by PC + offset x 4.
PC (program counter) is the location of our next address.
Conditional branches tend to branch to nearby instructions
  Some studies suggest half of all branches go less than 16 instructions away.

## Slide 99: PC-relative Addressing
Destination is determine by PC + offset x 4.
If we use PC as the register to be added to the address, our branch range will be 215 words in either direction.

## Slide 100: Pseudodirect Addressing
j 10000
  PC = PC31…28 : (address × 4)
  PC = PC31…28 : 40000
2
10000
6 bits
26 bits

## Slide 101: Pseudodirect Addressing
The 26-bit address field is shifted to the left twice
  Multiplies by four and creates a 28 bit field
  Four most significant bits are copied from the current PC

## Slide 102: Target Addressing Example
Loop code from earlier example
  Assume Loop at location 80000
Loop: sll $t1, $s3, 2 | 80000 | 0 | 0 | 19 | 9 | 4 | 0
add $t1, $t1, $s6 | 80004 | 0 | 9 | 22 | 9 | 0 | 32
lw $t0, 0($t1) | 80008 | 35 | 9 | 8 | 0 |  | 
bne $t0, $s5, Exit | 80012 | 5 | 8 | 21 | 2 |  | 
addi $s3, $s3, 1 | 80016 | 8 | 19 | 19 | 1 |  | 
j Loop | 80020 | 2 | 20000 |  |  |  | 
Exit: … | 80024 |  |  |  |  |  | 

## Slide 103: Decoding Machine Language
The first six bits are the opcode
R-type
I-type
J-type
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
op
address
6 bits
26 bits

## Slide 104: Decoding Machine Language
Based on the opcode:
  Bits 31-29 specify row
  Bits 28-26 specify column

## Slide 105: Decoding Machine Language
R-type instructions have an opcode of 000000
  Instruction is determined by funct field
  Bits 5-3 specify row
  Bits 2-0 specify column

## Slide 106: MIPS Integer Arithmetic
Why doesn’t MIPS have a subtract immediate instruction?
  Negative constants appear much less frequently in C and Java
  Since the immediate field holds both negative and positive constants, add immediate with a negative number is equivalent to subtract immediate with a positive number.

## Slide 107: Sort Example
void sort (int v[], int n) { int i, j; for (i=0; i<n; i++) for (j=i-1; j>= 0 && v[j] > v[j+1]; j--) swap(v, j); }
void swap(int v[], int k) { int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }

## Slide 108: Translate Swap (Leaf Procedure)
Allocate registers to program variables.
Produce code for the body of the procedure.
Preserve registers across the procedure invocation.

## Slide 109: Translate Swap (Leaf Procedure)
Allocate registers to program variables.
void swap(int v[], int k)
Base address of v in $a0
k in $a1
temp in $t0

## Slide 110: Translate Swap (Leaf Procedure)
Produce code for the body of the procedure.
swap:
sll $t1, $a1, 2 # $t1 = k * 4
add $t1, $a0, $t1 # $t1 = v+(k*4)
# (address of v[k])
lw $t0, 0($t1) # $t0 (temp) = v[k]
lw $t2, 4($t1) # $t2 = v[k+1]
sw $t2, 0($t1) # v[k] = $t2 (v[k+1])
sw $t0, 4($t1) # v[k+1] = $t0 (temp)
jr $ra # return to calling routine

## Slide 111: Translate sort
void sort (int v[], int n) { int i, j; for (i=0; i<n; i++) for (j=i-1; j>= 0 && v[j] > v[j+1]; j--) swap(v, j); }

## Slide 112: Translate sort – Outer for loop
for (i=0; i<n; i++)
add $s0, $zero, $zero #initialize i
for1:
slt $t0, $s0, $a1 #reg $t0 = 0 if $s0 >= $a1 (i>=n)
beq $t0, $zero,exit1 #go to exit1 if $s0>=$a1 (i>=n)
…
j for1 #jump to test of outer loop
exit1:

## Slide 113: Translate sort – Inner for loop
for (j=i-1; j>= 0 && v[j] > v[j+1]; j--)
addi $s1, $s0, –1 # j = i – 1
for2:
slti $t0, $s1, 0 # reg $t0 = 1 if $s1 < 0 (j<0)
bne $t0, $zero,exit2 # go to exit2 if $s1<0 (j<0)
sll $t1, $s1,2 # reg $t1 = j * 4
add $t2, $a0,$t1 # reg $t2 = v + (j * 4)
lw $t3, 0($t2) # reg $t3 = v[j]
lw $t4, 4($t2) # reg $t4 = v[j + 1]
slt $t0, $t4, $t3 # reg $t0 = 0 if $t4 >= $t3
beq $t0, $zero,exit2 # go to exit2 if $t4 >= $t3
...
addi $s1, $s1, –1 # j -= 1
j for2 # jump to test of inner loop
exit2:

## Slide 114: Translate sort – Calling Swap
Preserve contents of $a0 and $a1
  If we have unused registers, storing $a0 and $a1 there will be faster than storing on the stack
add $s2, $a0, $zero # copy parameter $a0 into $s2
add $s3, $a1, $zero # copy parameter $a1 into $s3
add $a0, $s2, $zero # first swap parameter is v
add $a1, $s1, $zero # second swap parameter is j
jal swap

## Slide 115: Translate sort – before the loops
Save registers when sort begins
addi $sp,$sp,–20 # make room on stack for 5 regs
sw $ra,16($sp) # save $ra on stack
sw $s3,12($sp) # save $s3 on stack
sw $s2, 8($sp) # save $s2 on stack
sw $s1, 4($sp) # save $s1 on stack
sw $s0, 0($sp) # save $s0 on stack

## Slide 116: Translate sort – after the loops
Restore registers when sort ends
lw $s0, 0($sp) # restore $s0 from stack
lw $s1, 4($sp) # restore $s1 from stack
lw $s2, 8($sp) # restore $s2 from stack
lw $s3,12($sp) # restore $s3 from stack
lw $ra,16($sp) # restore $ra from stack
addi $sp,$sp, 20 # restore stack pointer

## Slide 117: Translate Sort
sort:
addi $sp,$sp, –20 # make room on stack for 5 registers
sw $ra, 16($sp) # save $ra on stack
sw $s3,12($sp) # save $s3 on stack
sw $s2, 8($sp) # save $s2 on stack
sw $s1, 4($sp) # save $s1 on stack
sw $s0, 0($sp) # save $s0 on stack
add $s2, $a0, $zero # copy parameter $a0 into $s2
add $s3, $a1, $zero # copy parameter $a1 into $s3
add $s0, $zero, $zero # i = s0 = 0
for1:
slt $t0, $s0, $a1 # reg $t0 = 0 if $s0 >= $a1 (i>=n)
beq $t0, $zero,exit1 # go to exit1 if $s0􀁵$a1 (i>=n)
addi $s1, $s0, –1 # j = i – 1
for2:
slti $t0, $s1, 0 # reg $t0 = 1 if $s1 < 0 (j<0)
bne $t0, $zero,exit2 # go to exit2 if $s1<0 (j<0)
sll $t1, $s1,2 # reg $t1 = j * 4
add $t2, $a0,$t1 # reg $t2 = v + (j * 4)
lw $t3, 0($t2) # reg $t3 = v[j]
lw $t4, 4($t2) # reg $t4 = v[j + 1]
slt $t0, $t4, $t3 # reg $t0 = 0 if $t4 >= $t3
beq $t0, $zero,exit2 # go to exit2 if $t4 >= $t3
add $a0, $s2, $zero # first swap parameter is v
add $a1, $s1, $zero # second swap parameter is j
jal swap
addi $s1, $s1, –1 # j -= 1
j for2 # jump to test of inner loop
exit2:
addi $s0, $s0, 1 # i += 1
j for1 # jump to test of outer loop
exit1:
lw $s0, 0($sp) # restore $s0 from stack
lw $s1, 4($sp) # restore $s1 from stack
lw $s2, 8($sp) # restore $s2 from stack
lw $s3,12($sp) # restore $s3 from stack
lw $ra,16($sp) # restore $ra from stack
addi $sp,$sp, 20 # restore stack pointer
jr $ra # return to calling routine

## Slide 118: Translation and Startup
Many compilers produce object modules directly
Static linking

## Slide 119: Step 1: Compiling
A compiler transforms a high-level language into assembly instructions and pseudoinstructions
  High level languages use fewer lines of code
  Modern programmer productivity is higher
  Modern compilers are better at optimizing assembly language

## Slide 120: Assembler Pseudoinstructions
Pseudoinstructions: common variation of assembly language instructions
move $t0, $t1 → add $t0, $zero, $t1
blt $t0, $t1, L → slt $at, $t0, $t1 bne $at, $zero, L

## Slide 121: Step 2: Assembly
resolve labels on instructions and data:
  relative to PC for instructions
  relative to some register for data
  either two-pass or use backpatch to resolve external references and PC-relative spans
expand any macros and pseudoinstructions
handle any assembler directives: data layout
translate instructions to binary
create object file:
  headers
  code segment (called text in Unix)
  data segment
  relocation information: instruction/data words to relocate
  symbol table: unresolved references + visible symbols
  debugging information

## Slide 122: Step 3: Linking
Standard library routines are often not recompiled
The linker will use the already compiled version
Place code and data modules symbolically in memory.
Determine the addresses of data and instruction labels.
Patch both the internal and external references.
The result is an executable file with no unresolved references.

## Slide 123: Step 4: Loading
reads executable
loads code and data segments
initializes registers, stack, and arguments
jumps to program’s start-up routine to initiate execution

## Slide 124: Dynamic Linking
Static Linking Advantage
  fastest method to call library routines
Static Linking Disadvantages
  Routines become part of the executable code
    Updating is more difficult
    The whole library must be loaded
Dynamic linking postpones loading and linking library routines until the program is run.
  Very slow the first time the routine is called

## Slide 125: Summary - MIPS
32 general purpose registers
  Software conventions assign properties to registers
32-bit wide instructions
  3 formats: R-type, I-type, J-type
  Machine code: binary or hexadecimal
Reduced Instruction Set
  Operations: Arithmetic, Logical, Data Transfer, Conditional

## Slide 126: Summary – Design Issues
Simplicity favors regularity. Regularity motivates many features of the MIPS instruction set: keeping all instructions a single size, always requiring three register operands in arithmetic instructions, and keeping the register fields in the same place in each instruction format.
Smaller is faster. The desire for speed is the reason that MIPS has 32 registers rather than many more.

## Slide 127: Summary – Design Issues
Make the common case fast. Examples of making the common MIPS case fast include PC-relative addressing for conditional branches and immediate addressing for constant operands.
Good design demands good compromises. One MIPS example was the compromise between providing for larger addresses and constants in instructions and keeping all instructions the same length.