## Slide 1: Binary Representation

## Slide 2: Representations of Integers
In the modern world, we use decimal, or base 10, notation to represent integers.
We can represent numbers using any base b, where b is a positive integer greater than 1.

## Slide 3: Base 10
When we write 965, this can be translated as:
  9∙102 + 6∙101 + 5∙100

## Slide 4: Base 10
When we write 965, this can be translated as:
  9∙102 + 6∙101 + 5∙100
n = akbk + ak-1bk-1 + …. + a1b + a0

## Slide 5: Base b
Theorem: Let b be a positive integer greater than 1. Then if n is a positive integer, it can be expressed uniquely in the form:
n = akbk + ak-1bk-1 + …. + a1b + a0
where k is a nonnegative integer and a0,a1,…. ak are nonnegative integers less than b.
This representation of n is called the base b expansion of n and can be denoted by (akak-1….a1a0)b.
We usually omit the subscript 10 for base 10 expansions.

## Slide 6: Binary Expansions
Computers represent integers and do arithmetic with binary (base 2) expansions of integers. In these expansions, the only digits used are 0 and 1.

## Slide 7: Binary Expansions
Example: What is the decimal expansion of the integer that has (11011)2 as its binary expansion?
Solution:
(11011)2
= 1 ∙24 + 1∙23 + 0∙22 + 1∙21 + 1∙20
= 16 + 8 + 0 + 2 + 1
= 27.

## Slide 8: Binary Expansions
Example: What is the decimal expansion of the integer that has (1 0101 1111)2 as its binary expansion?
Solution:
(1 0101 1111)2
= 1∙28 + 0∙27 + 1∙26 + 0∙25 + 1∙24 + 1∙23 + 1∙22 + 1∙21 + 1∙20
= 256 + 0 + 64 + 0 + 16 + 8 + 4 + 2 + 1
= 351.

## Slide 9: Base Conversion
To construct the base b expansion of an integer n:
  Divide n by b to obtain a quotient and remainder.
    n = bq0 + a0 0 ≤ a0 < b

## Slide 10: Base Conversion
To construct the base b expansion of an integer n:
  Divide n by b to obtain a quotient and remainder.
    n = bq0 + a0 0 ≤ a0 < b
  The remainder, a0 , is the rightmost digit in the base b expansion of n.

## Slide 11: Base Conversion
To construct the base b expansion of an integer n:
  Divide n by b to obtain a quotient and remainder.
    n = bq0 + a0 0 ≤ a0 < b
  The remainder, a0 , is the rightmost digit in the base b expansion of n.
  Next, divide q0 by b.
    q0 = bq1 + a1 0 ≤ a1 < b

## Slide 12: Base Conversion
To construct the base b expansion of an integer n:
  Divide n by b to obtain a quotient and remainder.
    n = bq0 + a0 0 ≤ a0 < b
  The remainder, a0 , is the rightmost digit in the base b expansion of n.
  Next, divide q0 by b.
    q0 = bq1 + a1 0 ≤ a1 < b
  The remainder, a1, is the second digit from the right in the base b expansion of n.

## Slide 13: Base Conversion
To construct the base b expansion of an integer n:
  Divide n by b to obtain a quotient and remainder.
    n = bq0 + a0 0 ≤ a0 < b
  The remainder, a0 , is the rightmost digit in the base b expansion of n.
  Next, divide q0 by b.
    q0 = bq1 + a1 0 ≤ a1 < b
  The remainder, a1, is the second digit from the right in the base b expansion of n.
  Continue by successively dividing the quotients by b, obtaining the additional base b digits as the remainder. The process terminates when the quotient is 0.

## Slide 14: Base Conversion
Example: Find the binary expansion of (19)10
Solution: Successively dividing by 2 gives:
  19 = 2 * 9 + 1
  9 = 2 * 4 + 1
  4 = 2 * 2 + 0
  2 = 2 * 1 + 0
  1 = 2 * 0 + 1

## Slide 15: Base Conversion
Example: Find the binary expansion of (19)10
Solution: Successively dividing by 2 gives:
  19 = 2 * 9 + 1
  9 = 2 * 4 + 1
  4 = 2 * 2 + 0
  2 = 2 * 1 + 0
  1 = 2 * 0 + 1
The remainders are the digits: read from bottom to top to become the binary number from left to right
(10011)2.

## Slide 16: Base Conversion
Example: Find the binary expansion of (12345)10
Solution: Successively dividing by 2 gives:
  12345 = 2 * 6172 + 1
  6172 = 2 * 3086 + 0
  3086 = 2 * 1543 + 0
  1543 = 2 * 771 + 1
  771 = 2 * 385 + 1
  385 = 2 * 192 + 1
  192 = 2 * 96 + 0
  96 = 2 * 48 + 0
  48 = 2 * 24 + 0
  24 = 2 * 12 + 0
  12 = 2 * 6 + 0
  6 = 2 * 3 + 0
  3 = 2 * 1 + 1
  1 = 2 * 0 + 1
(12345)10 = (11 0000 0011 1001)2

## Slide 17: List of Binary Numbers
Decimal | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
These are 4-bit unsigned binary numbers.

## Slide 18: Binary Addition
Binary number can be added the same way decimal numbers are added:

## Slide 19: Binary Addition
Binary number can be added the same way decimal numbers are added:
3 + 2 = 5
0 0 1 1
+ 0 0 1 0

## Slide 20: Binary Addition
Binary number can be added the same way decimal numbers are added:
3 + 2 = 5
0 0 1 1
+ 0 0 1 0
1

## Slide 21: Binary Addition
Binary number can be added the same way decimal numbers are added:
3 + 2 = 5
1
0 0 1 1
+ 0 0 1 0
0 1

## Slide 22: Binary Addition
Binary number can be added the same way decimal numbers are added:
3 + 2 = 5
1
0 0 1 1
+ 0 0 1 0
1 0 1

## Slide 23: Binary Addition
Binary number can be added the same way decimal numbers are added:
3 + 2 = 5
0 0 1 1
+ 0 0 1 0
0 1 0 1

## Slide 24: Binary Addition
Binary number can be added the same way decimal numbers are added:
3 + 3 = 6
0 0 1 1
+ 0 0 1 1

## Slide 25: Binary Addition
Binary number can be added the same way decimal numbers are added:
3 + 3 = 6
1
0 0 1 1
+ 0 0 1 1
0

## Slide 26: Binary Addition
Binary number can be added the same way decimal numbers are added:
3 + 3 = 6
1 1
0 0 1 1
+ 0 0 1 1
1 0

## Slide 27: Binary Addition
Binary number can be added the same way decimal numbers are added:
3 + 3 = 6
1 1
0 0 1 1
+ 0 0 1 1
1 1 0

## Slide 28: Binary Addition
Binary number can be added the same way decimal numbers are added:
3 + 3 = 6
0 0 1 1
+ 0 0 1 1
0 1 1 0

## Slide 29: Binary Subtraction
How do we subtract numbers?
7 – 6 = 7 + (-6) = 1
We need a way to represent negative numbers

## Slide 30: Signed Binary Numbers
To represent a negative number, we use a sign bit.
The sign bit is the most significant bit (MSB)
  1 represents a negative number
  0 represents a positive number

## Slide 31: Signed Representations
Sign-Magnitude: sign bit + absolute value
  Positive 7 0111
  Negative 7 1111
1’s Complement: bitwise inverse
  Positive 7 0111
  Negative 7 1000
Disadvantages
  Two representations for 0: +0, -0
  Arithmetic is more complex
Advantages
  The magnitude (absolute value) of the smallest number is the same as the largest number

## Slide 32: 2’s Complement Representation
To represent a negative value: do a bitwise inverse, then add 1
To determine -7:
  7 0111
  Bitwise inverse 1000 Add 1 1001
2’s Complement is the standard representation for negative numbers.

## Slide 33: Binary Numbers
Decimal | Binary | Decimal | Binary
0 | 0000 | -1 | 1111
1 | 0001 | -2 | 1110
2 | 0010 | -3 | 1101
3 | 0011 | -4 | 1100
4 | 0100 | -5 | 1011
5 | 0101 | -6 | 1010
6 | 0110 | -7 | 1001
7 | 0111 | -8 | 1000
List of Binary Numbers in 2’s Complement Representation
4 bits gives us the following range:
Biggest 4-bit number: 7
Smallest 4-bit number: -8

## Slide 34: Binary Subtraction
2’s complement binary numbers are subtracted by adding their negative equivalent.
7 – 6 = 7 + (-6) = 1
0 1 1 1
+ 1 0 1 0

## Slide 35: Binary Subtraction
Binary numbers are subtracted by adding their 2’s complement equivalent.
7 – 6 = 7 + (-6) = 1
0 1 1 1
+ 1 0 1 0
1

## Slide 36: Binary Subtraction
Binary numbers are subtracted by adding their 2’s complement equivalent.
7 – 6 = 7 + (-6) = 1
1
0 1 1 1
+ 1 0 1 0
0 1

## Slide 37: Binary Subtraction
Binary numbers are subtracted by adding their 2’s complement equivalent.
7 – 6 = 7 + (-6) = 1
1 1
0 1 1 1
+ 1 0 1 0
0 0 1

## Slide 38: Binary Subtraction
Binary numbers are subtracted by adding their 2’s complement equivalent.
7 – 6 = 7 + (-6) = 1
1 1 1
0 1 1 1
+ 1 0 1 0
0 0 0 1

## Slide 39: Binary Subtraction
Binary numbers are subtracted by adding their 2’s complement equivalent.
7 – 6 = 7 + (-6) = 1
1
0 1 1 1
+ 1 0 1 0
0 0 0 1
The extra 1, called the carry-out, is ignored

## Slide 40: Overflow
Overflow occurs when the result of an arithmetic operation is too large or too small to represent.
  In our 4-bit examples, that would occur if the result is less than -8 or greater than 7.

## Slide 41: Overflow
Overflow occurs when adding whenever:
  2 positive numbers are added and the result is negative
  2 negative numbers are added and the result is positive

## Slide 42: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.

## Slide 43: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
7 – 6 = 7 + (-6) = 1
1 1 1
0 1 1 1
+ 1 0 1 0
0 0 0 1
Most Significant Bit
Carry In
Carry Out
Since the Carry in of the MSB is equal to the carry out, no overflow has occurred. The carry out is discarded and “0001” is the correct result.

## Slide 44: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
7 + 3 = 10
0 1 1 1
+ 0 0 1 1

## Slide 45: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
7 + 3 = 10
1
0 1 1 1
+ 0 0 1 1
0

## Slide 46: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
7 + 3 = 10
1 1
0 1 1 1
+ 0 0 1 1
1 0

## Slide 47: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
7 + 3 = 10
1 1 1
0 1 1 1
+ 0 0 1 1
0 1 0

## Slide 48: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
7 + 3 = 10
0 1 1 1
0 1 1 1
+ 0 0 1 1
1 0 1 0

## Slide 49: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
7 + 3 = 10
0 1 1 1
0 1 1 1
+ 0 0 1 1
1 0 1 0
Most Significant Bit
Carry In
Carry Out
Since the Carry in of the MSB is not equal to the carry out, an overflow has occurred.
The result calculated (-6) is clearly incorrect.

## Slide 50: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
-4 - 5 = -9
1 1 0 0
+ 1 0 1 1

## Slide 51: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
-4 - 5 = -9
1 1 0 0
+ 1 0 1 1
1

## Slide 52: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
-4 - 5 = -9
1 1 0 0
+ 1 0 1 1
1 1

## Slide 53: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
-4 - 5 = -9
1 1 0 0
+ 1 0 1 1
1 1 1

## Slide 54: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
-4 - 5 = -9
1
1 1 0 0
+ 1 0 1 1
0 1 1 1

## Slide 55: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
-4 - 5 = -9
1 0
1 1 0 0
+ 1 0 1 1
0 1 1 1
Most Significant Bit
Carry In
Carry Out
Since the Carry in of the MSB is not equal to the carry out, an overflow has occurred.
The result calculated (7) is clearly incorrect.

## Slide 56: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
3 + (-5) = -2
0 0 1 1
+ 1 0 1 1

## Slide 57: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
3 + (-5) = -2
1
0 0 1 1
+ 1 0 1 1
0

## Slide 58: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
3 + (-5) = -2
1 1
0 0 1 1
+ 1 0 1 1
1 0

## Slide 59: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
3 + (-5) = -2
0 1 1
0 0 1 1
+ 1 0 1 1
1 1 0

## Slide 60: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
3 + (-5) = -2
0 0 1 1
0 0 1 1
+ 1 0 1 1
1 1 1 0

## Slide 61: Overflow
An easy way to spot overflow is to compare the “Carry in” of the MSB to the “Carry out”. If they are different, then overflow has occurred.
3 + (-5) = -2
0 0 1 1
0 0 1 1
+ 1 0 1 1
1 1 1 0
Most Significant Bit
Carry In
Carry Out
Since the Carry into of the MSB is equal to the carry out, no overflow has occurred. The extra zero is discarded and “1110” is the correct result.